## Slide 1: Square & Triangular Wave Generator
Yousef AlAbdulrazzaq 75018
Hamad AlAjmi 10081835
Mohammad AlDosari 74123

## Slide 2: Abstract
Generate square and triangular waveforms using LM371 op-amps
Show that integrating a square wave results in a triangular wave
Design a working prototype and verify through simulation

## Slide 3: Theory (Square Wave)
Power on  Output goes to +Vcc
C1 charges through R1
C1 voltage exceeds threshold  Output flips to –Vcc
C1 discharges
C1 drops below negative threshold  Output flips to +Vcc
Cycle repeats producing square waveform
[1]

## Slide 4: Theory (Integrator)
Square wave input through R4
Operation:
  Constant positive input  Output ramps down linearly
  Constant negative input  Output ramps up linearly
  Alternating +/- from square wave creates triangular wave

## Slide 5: Criteria & Constraints
Criteria:
  Generate stable square waveform
  Integrate square wave into triangular waveform
  Only use op-amps and passive components
Constraints:
  Circuit does not have external input
  Use of standard RC components

## Slide 6: Block Diagram
U2
Integrator
U1
Square Wave Generator
Triangular Waveform
∫
Square Waveform

## Slide 7
R1 would be a 10kΩ potentiometer

## Slide 8: Component Justification
R1 is a potentiometer which allows for adjustable frequency
R2 = R3 sets[2]
  This means 50% of the output voltage is fed back to pin 3
  The thresholds are +6V & -6V and the charge & discharge time are equal
R4 controls charging rate of C2
R5 must be much larger than R4 to prevent integrator saturation
R6 is used to fix pin 3 of U2 at 0V, providing a stable reference point
C1 easy to observe on oscilloscope
C2 smaller value results in larger amplitude of waveform

## Slide 9: Expected Results
If R1 is set to 1kΩ, the resultant frequency for both waveforms will be about 45Hz
The amplitude of both waveforms will be about ±11V
  Saturation voltage is slightly less than ±12V supply
The waveforms’ rise and
fall time should be equal
[3]

## Slide 10: Conclusion
Successfully generated a square waveform
Correctly integrated the square wave into a triangular waveform
Designed a stable and simple circuit ready for prototyping

## Slide 11: References
[1] Tutorialspoint, "Linear Integrated Circuits Applications - Waveform Generators," Tutorialspoint, 2024. [Online]. Available: https://www.tutorialspoint.com/linear_integrated_circuits_applications/linear_integrated_circuits_applications_waveform_generators.htm.
[2] AspenCore, Inc., "Negative Feedback Systems," Electronics Tutorials, 2024. [Online]. Available: https://www.electronics-tutorials.ws/systems/negative-feedback.html.
[3] AspenCore, Inc., "Op-amp Multivibrator," Electronics Tutorials, 2024. [Online]. Available: https://www.electronics-tutorials.ws/opamp/op-amp-multivibrator.html.