## Slide 1: Digital Robotic Sensor on FPGA
CE/EE 270 Introduction to Digital System Design
Project Deliverable 1
Spring 2026
AbdulRahman Ahmed 10095516
Yousef AlAbdulrazzaq 75018

## Slide 2
Contents
Introduction
1
Block Diagram
2
Function Table
3
Motor Speed
4
Conclusion
10
Turning Angle
5
Sensor Compare
6
Directions
7
Difference
8
System Off
9
Notes: Quick agenda. We'll start with the problem statement and the assumptions we made when interpreting overflow. Then we'll show the block diagram and walk through the function table that lists all eight operations. After that we go one by one through each operation, showing the truth table, K-map, and the simplified equation. We close with the Verilog and a short conclusion.

## Slide 3: Problem Statement and Design Assumptions
Problem
Design an FPGA module with two 3-bit sensor inputs (G and Y) and a 3-bit function selector (S) that supports 8 distinct operations. The output drives one 7-segment display and an overflow LED.
Display Encoding D[3:0]
Code | Symbol | Meaning
0000 to 0111 | 0 to 7 | Numeric digit
1000 | E | Compare equal
1001 | U | Compare not-equal
1100 | = | Overflow
1011 | blank | System off
Design Assumptions
Overflow interpretation
A 3-bit input maxes out at 7, so the input itself can't exceed range. We treat overflow as the COMPUTED RESULT exceeding 7.
Subtraction underflow
For G − Y, when Y > G the result would be negative. The overflow LED activates and the display shows "=".
Display drive
Active-LOW segments per the DE-series Altera FPGA convention. A bit value of 0 means the segment is ON.
Notes: Here's the problem. We've got two 3-bit sensor inputs called G and Y, plus a 3-bit selector S. The module has to do eight different things based on S, and the result lights up a single 7-segment display along with an overflow LED.
A few decisions we had to make. First, since 3-bit inputs cap at 7, "overflow" can't mean the input is too big. We defined it as the computed result going above 7, like 2 times G when G is 5 or more. Second, for subtraction we treat Y greater than G as overflow too, because the result would go negative. Third, the segments on the DE-series board are active low, so a zero in our HEX output actually turns a segment on.
The encoding scheme on the left shows how D maps to the display. Codes zero through seven are just digits. Then we use four extra codes for E, U, the equals sign for overflow, and blank for off.

## Slide 4: System Block Diagram
Bus widths shown by slash + number
D[3:0] = display code
HEX[6:0] = active-LOW segments
Notes: This is the top-level architecture. Three inputs on the left feed into the Robotic Sensor Processing block in the center. G and Y are the 3-bit sensor readings. S is the 3-bit selector that picks which of the eight operations runs.
Processing produces two outputs. D is a 4-bit display code that goes through the 7-Segment Decoder, and from there the 7-bit HEX bus drives the display. The OF flag goes straight to the Overflow LED.
We added the explicit OF path to the LED because the project requires us to indicate when results go out of range. The bus widths are shown by the slash and number on each wire, which is standard digital schematic notation.

## Slide 5: Function Table for the 8 Operations
S[2:0] selects the operation. G and Y are the 3-bit sensor inputs. D[3:0] is the display code, OF is the overflow flag.
S[2:0] | Operation | Computed Output | Display when valid | Overflow Condition
000 | Motor Speed | 2 · G | 2G as digit (0–6) | G ≥ 4
001 | Turning Angle | 3 · Y | 3Y as digit (0, 3, 6) | Y ≥ 3
010 | Sensor Compare | E if G = Y else U | E or U | never
011 | Forward Adjust | G + 3 | G+3 as digit (3–7) | G ≥ 5
100 | Clearance | 7 − Y | (7−Y) as digit | never
101 | Path Average | ⌊(G + Y) / 2⌋ | avg as digit (0–7) | never
110 | Difference | G − Y | (G−Y) as digit | Y > G
111 | System Off | none | blank | never
Notes: This is the master table. Each row is one operation, picked by the 3-bit selector S.
The first four operations cover motor speed, turning angle, sensor compare, and forward adjust. Motor speed is two times G, used to drive the wheels faster when the front sensor reads high. Turning angle is three times Y for the side sensor. Compare just tests whether G equals Y and shows E or U. Forward adjust is G plus three, a small offset bias.
The next three are clearance, path average, and difference. Clearance is seven minus Y, useful for inverting a proximity reading. Path average is the floor of G plus Y over two. Difference is G minus Y, with overflow when Y is bigger than G because the result would go negative.
The last operation, system off, just blanks the display. Notice five of the eight ops can overflow, and three never do, including the average since the max is still seven.

## Slide 6: Motor Speed (S = 000)
Front sensor scaled by 2 for drive output. Overflows when 2G ≥ 8 (i.e. G ≥ 4).
G[2:0] | 2·G | D[3:0] | OF
000 | 0 | 0000 | 0
001 | 2 | 0010 | 0
010 | 4 | 0100 | 0
011 | 6 | 0110 | 0
100 | OF | 1100 | 1
101 | OF | 1100 | 1
110 | OF | 1100 | 1
111 | OF | 1100 | 1
K-map for D[3]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
D[3] = G[2]
K-map for D[2]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
D[2] = G[2] + G[1]
K-map for D[1]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
D[1] = G[2]'·G[0]
K-map for D[0]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
D[0] = 0
K-map for OF
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
OF = G[2]
D[3:0] = { G[2], G[2]+G[1], G[2]'·G[0], 0 } OF = G[2]
Notes: First operation, motor speed. The front sensor reading G gets multiplied by two before driving the motors.
The truth table on the left shows what happens for each G. From zero through three, two times G fits in the four-bit display fine. Once G reaches four, the result is eight or higher, which can't fit, so we set the overflow flag and force the display to one-one-zero-zero, our overflow code.
Now the five K-maps on the right break the four-bit output into individual bit equations. D three is the simplest, just G two, since the bottom row is all ones. D two has two overlapping groups, the bottom row plus the right pair of columns, simplifying to G two plus G one. D one needs a small group of two on the top row, giving G two prime times G zero. D zero is constant zero everywhere. And the overflow flag matches D three exactly, both equal to G two.
When you put these together, the assembly at the bottom shows the full four-bit output as a function of the input bits.

## Slide 7: Turning Angle (S = 001)
Side sensor scaled by 3 for steering. Overflows when 3Y ≥ 8 (i.e. Y ≥ 3).
Y[2:0] | 3·Y | D[3:0] | OF
000 | 0 | 0000 | 0
001 | 3 | 0011 | 0
010 | 6 | 0110 | 0
011 | OF | 1100 | 1
100 | OF | 1100 | 1
101 | OF | 1100 | 1
110 | OF | 1100 | 1
111 | OF | 1100 | 1
K-map for D[3]
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
D[3] = Y[2] + Y[1]·Y[0]
K-map for D[2]
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
D[2] = Y[2] + Y[1]
K-map for D[1]
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
D[1] = Y[2]'·(Y[1]⊕Y[0])
K-map for D[0]
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0
D[0] = Y[2]'·Y[1]'·Y[0]
K-map for OF
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
OF = Y[2] + Y[1]·Y[0]
D[3]=Y[2]+Y[1]Y[0] D[2]=Y[2]+Y[1] D[1]=Y[2]'(Y[1]⊕Y[0]) D[0]=Y[2]'Y[1]'Y[0] OF=D[3]
Notes: Turning angle multiplies Y by three. From the truth table, only Y of zero, one, and two give valid display values. Once Y hits three, three Y is nine, which exceeds seven, so we go to overflow.
The K-maps tell the story bit by bit. D three has two groups, the whole bottom row plus a vertical pair in the third column, giving Y two plus the AND of Y one and Y zero. D two simplifies cleanly to Y two plus Y one. D one is interesting because the two ones in the K-map are not adjacent, so they form an XOR pattern, and we factor out Y two prime. D zero is a single minterm at the cell where Y is zero zero one. Overflow matches D three exactly.

## Slide 8: Sensor Compare (S = 010)
Tests whether front and side sensors agree. Output is "E" when equal, "U" otherwise. Builds on the Chapter 4 equality comparator. Never overflows.
G[2:0] | Y[2:0] | Result | D[3:0]
000 | 000 | equal | 1000
010 | 010 | equal | 1000
111 | 111 | equal | 1000
001 | 010 | not eq | 1001
100 | 011 | not eq | 1001
011 | 111 | not eq | 1001
Chapter 4 building block — 1-bit equality cell (XNOR)
G[i]
Y[i]
XNOR
eq[i] = G[i]⊙Y[i]
eq[i] = 1 when bit i matches
3-bit equality: AND the per-bit equalities
eq = (G[2]⊙Y[2]) · (G[1]⊙Y[1]) · (G[0]⊙Y[0])
Per-bit outputs (from encoding E=1000, U=1001)
D[3] = 1 (constant) D[2] = 0 (constant)
D[1] = 0 (constant) D[0] = NOT(eq)
OF = 0 (constant)
D[3:0] = { 1, 0, 0, eq' } where eq = (G[2]⊙Y[2])·(G[1]⊙Y[1])·(G[0]⊙Y[0]) OF = 0
Notes: Sensor compare checks if G equals Y. We can't draw a single K-map for this because the truth table has six input variables, sixty-four rows, way beyond a Chapter three K-map.
Instead, we use the Chapter four equality comparator. The basic building block is a one-bit equality cell, which is just an XNOR gate. When the two bits match, the output is one. We chain three of these in parallel, one per bit position, and AND their outputs. The result is the equality flag.
For the display output, we pre-decided that E equals one zero zero zero and U equals one zero zero one. So three of the four output bits are constants, and only D zero changes. D zero is the inverted equality flag, so D zero is one when the bits don't match.

## Slide 9: Forward Adjust (S = 011)
Adds a bias of 3 to G for nudging forward. Overflows when G+3 ≥ 8 (i.e. G ≥ 5).
G[2:0] | G+3 | D[3:0] | OF
000 | 3 | 0011 | 0
001 | 4 | 0100 | 0
010 | 5 | 0101 | 0
011 | 6 | 0110 | 0
100 | 7 | 0111 | 0
101 | OF | 1100 | 1
110 | OF | 1100 | 1
111 | OF | 1100 | 1
K-map for D[3]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
D[3] = G[2]·(G[1]+G[0])
K-map for D[2]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
D[2] = G[2]+G[1]+G[0]
K-map for D[1]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0
D[1] = G[1]'·G[0]'+G[2]'·G[1]·G[0]
K-map for D[0]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 0 | 0
D[0] = G[0]'·(G[1]'+G[2]')
K-map for OF
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 1
OF = G[2]·(G[1]+G[0])
D[3]=G[2](G[1]+G[0]) D[2]=G[2]+G[1]+G[0] D[1]=G[1]'G[0]'+G[2]'G[1]G[0] D[0]=G[0]'(G[1]'+G[2]') OF=D[3]
Notes: Forward adjust adds three to G. From G of zero up to G of four, the result fits in the display. Once G is five or higher, G plus three is eight or more, so we overflow.
The five K-maps work out the per-bit equations. D three has two overlapping groups in the bottom row, which factor as G two times the OR of G one and G zero. D two is one almost everywhere, only zero at G equals zero zero zero, so it simplifies to a three-input OR. D one is harder, with three ones not all adjacent, so we end up with a sum of two product terms. D zero uses a wrap-around group across the leftmost and rightmost columns of the top row, plus a vertical pair on the left edge. Notice the overflow K-map matches D three exactly.

## Slide 10: Clearance (S = 100)
Computes 7 − Y to invert a proximity reading. Result is always 0–7, never overflows.
Y[2:0] | 7−Y | D[3:0] | OF
000 | 7 | 0111 | 0
001 | 6 | 0110 | 0
010 | 5 | 0101 | 0
011 | 4 | 0100 | 0
100 | 3 | 0011 | 0
101 | 2 | 0010 | 0
110 | 1 | 0001 | 0
111 | 0 | 0000 | 0
K-map for D[3]
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
D[3] = 0
K-map for D[2]
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
D[2] = Y[2]'
K-map for D[1]
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0
D[1] = Y[1]'
K-map for D[0]
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 1 | 0 | 0 | 1
1 | 1 | 0 | 0 | 1
D[0] = Y[0]'
K-map for OF
Y[1]Y[0]\Y[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
OF = 0
D[3:0] = { 0, Y[2]', Y[1]', Y[0]' } = { 0, ~Y[2:0] } OF = 0
Notes: Clearance is seven minus Y. There's a beautiful identity hiding here. For any three-bit Y, seven minus Y equals the bitwise NOT of Y. You can see this directly in the truth table, where the lower three bits of D are exactly Y inverted bit by bit.
The K-maps confirm this. D three is all zeros since the result never reaches eight. D two is one wherever Y two is zero, which is the whole top row, giving Y two prime. D one is the same pattern but on Y one, simplifying to Y one prime. D zero needs the famous wrap-around group spanning the leftmost and rightmost columns, and that gives Y zero prime.
Because seven minus Y is always non-negative, the overflow flag is constantly zero.

## Slide 11: Path Average (S = 101)
Computes ⌊(G+Y)/2⌋ for sensor averaging. Max average is 7, so never overflows.
G[2:0] | Y[2:0] | G+Y | avg | D[3:0]
000 | 000 | 0 | 0 | 0000
001 | 011 | 4 | 2 | 0010
010 | 100 | 6 | 3 | 0011
011 | 011 | 6 | 3 | 0011
100 | 101 | 9 | 4 | 0100
110 | 110 | 12 | 6 | 0110
111 | 111 | 14 | 7 | 0111
Chapter 4 building block — 3-bit ripple-carry adder
3-bit Adder (3 full-adders chained)
G
Y
sum[3:0]
Right-shift by 1 (drops LSB) — pure wire reroute, no logic
sum[3] | → | D[2]
sum[2] | → | D[1]
sum[1] | → | D[0]
(sum[0]) | → | discarded
 |  | D[3] = 0, OF = 0
sum[3:0] = G + Y D[3:0] = { 0, sum[3], sum[2], sum[1] } OF = 0
Notes: Path average computes the floor of G plus Y over two. With both inputs three bits wide, the maximum sum is fourteen, which gives an average of seven. Seven still fits in the display, so this operation never overflows.
The implementation reuses two Chapter four building blocks. First, a three-bit ripple-carry adder produces a four-bit sum. Then the right shift by one is just a wire reroute: we take the upper three bits of the sum and route them to D bits two, one, and zero. The least significant sum bit is discarded because the floor operation drops it. D three stays at zero since the maximum result is seven.
This is cleaner than per-bit K-maps because the function has six input variables, and a six-variable K-map is impractical at Chapter three level.

## Slide 12: Difference (S = 110)
Computes G − Y. When Y > G, OF activates and display shows overflow.
G[2:0] | Y[2:0] | Case | D[3:0] | OF
111 | 011 | G > Y | 0100 | 0
101 | 010 | G > Y | 0011 | 0
100 | 100 | G = Y | 0000 | 0
010 | 010 | G = Y | 0000 | 0
001 | 011 | Y > G | 1100 | 1
010 | 110 | Y > G | 1100 | 1
000 | 111 | Y > G | 1100 | 1
Chapter 4 building blocks — magnitude comparator + 3-bit subtractor
3-bit Magnitude Comparator
OF = (Y > G)
3-bit Subtractor (G − Y)
diff[2:0] = G−Y
Output mux on OF flag
D[3] = OF D[2] = OF + diff[2]
D[1] = OF'·diff[1] D[0] = OF'·diff[0]
When OF = 1: D = 1100 (overflow)
When OF = 0: D = { 0, diff[2:0] }
OF = (Y > G) diff[2:0] = G − Y D[3:0] = OF ? 1100 : { 0, diff[2:0] }
Notes: Difference is G minus Y. We only get a valid display when G is at least Y. If Y is bigger, the result would go negative, and we flag overflow.
Two Chapter four blocks make this clean. The three-bit magnitude comparator inspects bits from the most significant downward, comparing them in pairs. Its single-bit output is the overflow flag, true when Y is greater than G.
In parallel, a three-bit subtractor computes G minus Y. Its output is only meaningful when no underflow happens, but we compute it anyway and select between it and the overflow code using a multiplexer driven by the comparator output. When OF is one, the display shows one one zero zero. When OF is zero, the display is zero followed by the three-bit difference.

## Slide 13: System Off (S = 111)
Disables sensors and blanks the display. All outputs are constants, independent of G and Y.
Inputs | D[3:0] | OF | 7-seg display
G, Y don't care | 1011 | 0 | blank
Why this code
Encoding 1011 is reserved for "blank" in our display map. The 7-segment decoder maps 1011 to all segments off.
K-maps for constants
Each output is a constant function of the inputs. The K-map for a constant has all cells filled with the same value. This is the trivial limit of the SOP method — no minterms means output 0; all minterms means output 1.
K-map for D[3]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
D[3] = 1
K-map for D[2]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
D[2] = 0
K-map for D[1]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
D[1] = 1
K-map for D[0]
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1
D[0] = 1
K-map for OF
G[1]G[0]\G[2] | 00 | 01 | 11 | 10
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0
OF = 0
D[3:0] = 1011 (blank) OF = 0 [outputs are constants, independent of G, Y]
Notes: System off is the simplest operation. When S is one one one, we ignore the sensor inputs entirely and blank the display.
The five small K-maps illustrate that constants are the trivial case of the K-map method. D three, D one, and D zero are constant ones, so every cell of their K-map is shaded. D two and the overflow flag are constant zeros, so every cell stays white. There's no minimization to do because the function does not depend on the inputs.
The display code one zero one one is reserved in our encoding for blank. The seven-segment decoder maps it to all segments off, which is what we want when the system is powered down.

## Slide 14: Verilog Implementation
Three modules synthesized in Quartus. Top module wires the system I/O. Robotic Sensor Processing implements the 8 operations via a case statement on S[2:0]. The 7-Segment Decoder maps each 4-bit display code to active-LOW segment outputs.
Top Module: System I/O
Robotic Sensor Processing
7-Segment Decoder
Notes: We split the design into three Verilog modules. Each one shows up as its own screenshot once we compile in Quartus.
The top module on the left is short. It just declares the I/O ports for G, Y, S, the HEX bus to the display, and the overflow LED, then instantiates the two sub-modules and wires them together.
The middle screenshot is the heart of the design, the Robotic Sensor Processing module. It's an always-comb block with a case statement on S. Each branch handles one of the eight operations and produces both D and OF in the same step.
The right one is the 7-segment decoder. It takes the 4-bit display code and maps it to the seven segment outputs. Codes zero through seven give standard digits. Codes 1000 through 1010 give the E, U, and equals symbols. Code 1011 gives a blank display.

## Slide 15: Conclusion
Summary
We designed a Digital Robotic Sensor Processor on FPGA that supports 8 sensor-driven operations and detects out-of-range results with an overflow LED.
The system takes two 3-bit sensors and a 3-bit selector, computes the chosen function, and drives a 7-segment display plus the overflow indicator.
Five of the eight operations can overflow; the other three (compare, clearance, average) always stay in range by design.
Achievements
Truth tables and K-maps
Derived for all 8 functions; SOP/POS forms documented.
Simplified Boolean and arithmetic equations
Expressed each output bit in its minimal form.
Three-module Verilog HDL
Top module, Robotic Sensor Processing, 7-Segment Decoder.
Custom 7-segment encoding
Digits 0–7 plus "E", "U", "=", and blank states.
Notes: To wrap up. We built a digital robotic sensor processor that takes in two sensor readings and a function selector, runs one of eight operations, and drives a display plus an overflow LED.
On the design side we derived truth tables and K-maps for every operation, then pulled out the simplest equations from each. For the arithmetic ops, the equations are arithmetic. For the boolean ops they're SOP minimizations. The Verilog implementation lives in three modules, one for I/O, one for the processing logic, and one for the segment decoder.
Five of the eight operations can overflow, and we handled that with a dedicated overflow code on the display and a separate LED. The other three, compare, clearance, and path average, are designed to always stay in the zero through seven range, so they never need the overflow path.
That's our design. Happy to take questions on any part of it.